## Slide 1: Reading ECG
Summary by Thomas Tay
Adapted from The EKG guy

## Slide 2: ECG course 2.0 – The heart ant its electrical conduction system
RV = most of anterior view of heart
Heart = 4 chamber pump
SA node  internodal pathways (anterior, middle, posterior)  AV node  Bundle of His  (LBB (LAF + LPF) + RBB)  Purkinje fibers
SA node = pacemaker of heart
Backup conduction system of the heart

## Slide 3: ECG course 3.0 – Electrophysiology of the heart
Base concentrations
  Inside: More K
  Outside: More Na and Ca
Phase 0 – Fast Na channels open, Na enters cardiomyocyte
Phase 1 – Cl channels open, Cl enters cardiomyocyte
Phase 2 – Slow Na channels and Ca channels open, Na and Ca flows into cell
Phase 3 – Fast K channels open, K flows out of the cell
Phase 4 – Below threshold, slowly rising to threshold due to higher positive charge outside

## Slide 4: ECG course 4.0 – Vectors and Electrodes
Deflection on ECG
  When a positive charge moves away from electrode, ECG deflects downwards
  When a positive charge moves towards an electrode, ECG deflects upwards
  When a positive charge moves across an electrode, ECG deflects upwards then downwards
Which ECG leads view which parts of the heart
  Leads II, III, aVF – inferior part of the heart
  Leads V1, V2 – septal part of the heart
  Leads V3, V4 - anterior part of the heart
  Leads V5, V6, I, aVL – lateral part of the heart

## Slide 5: ECG course 5.0 – EKG paper
Horizontal
  1 small box = 0.04s
  1 big box – 0.2s
  Time between 2 black lines = 1 sec
Vertical
  10 small box = 1mV
Calibrations
  Standard (25mm/s, 10 small box = 1mV)
  Half Standard (25mm/s, 10 small box = 2mV)
  50mm/s
12-lead ECG
  Each lead measured over 2.5 seconds
  Full stretch measured over 10 seconds
  Everything in a vertical line happened at the same time